## Slide 1
Bundle Adjustment
Math Reading
Seminar
Thing
LukášP

## Slide 2: Talk structure
3D geometry
Projective geometry
Problem Statement
Minimum Geometric Problems
Least squares, Moore-Penrose pseudoinverse, SVD
Nonlinear Least Squares
Intermezzo I – computing derivatives
  Symbolic / Numerical differentiation
  Dual numbers
  Lie groups basics
Handling Severe Nonlinearity
  Levenberg Marquardt
  Dogleg
Handling outliers – robust estimation
Intermezzo II – solving linear systems
  Direct methods
  Schur complement trickery
  Iterative methods
  Inexact step NLS
Calculating covariances

## Slide 3: 3D Geometry
Position representations
  Euclidean 3D
  Inverse depth 3D
  Inverse distance , where 1D
Rotation representations
  Rotation matrix 9D
    Hard to constrain orthogonality in numerical manipulation
  (Unit) Quaternion 4D
    Double cover of SO(3)!
  Axis-angle 3D
  Exponential map of (3) 3D

## Slide 4: Projective Geometry
Use homogenous coordinates
  [x/w, y/w, z/w]  [x, y, z, w]
Projection matrix
  Vision
  OpenGL
We‘re not interested in the w coordinate (it is „always“ 1).
Leads to division by depth.

## Slide 5: Pinhole Camera Model
Stolen from Bronek Pribyl‘s VGE lecture (I think)
P
principal axis
image plane
camera
centre
x
X
dimension
wrangling
magic
pose
intrinsics K
= K [R t]

## Slide 6: Other Camera Models
Spherical
Curvilinear
Catadioptric
…

## Slide 7: Lens Distortion Models
Brown's radial distortion model
  Here, is typically a polynomial function, e.g.: , where is a vector of polynomial coefficients

## Slide 8: Lens Distortion Models
Problem with invertibility of polynomial
Use analytical solution for low degrees
Otherwise use gradient descent

## Slide 9: Problem Statement
Bundle Adjustment
  „Having a lot of images of a scene, let‘s build a 3D model“
  Sparse approach (bundler)
    Find interest point in the images
    Match the interest points
    Calculate spatial rotation / translation between images
    Triangulate points
  Semi-dense approach (LSD)
    Somehow triangulate points in the first camera pair
    Color the points (from image pixels)
    For following cameras, reproject the 3D points, optimize rotation / translation to minimize color difference
  Dense approach (PMVS / CMVS)

## Slide 10: Problem Statement
Bundle Adjustment
  „Having a lot of images of a scene, let‘s build a 3D model“
  Sparse approach (bundler)
  Semi-dense approach (LSD)
  Dense approach (PMVS / CMVS)
    Solve dense pixel correspondences
    Early methods modifications of dynamic programming
    Gives per-pixel dense depth
      Requires known relative camera poses (ok for stereo)
    Can solve alignment by e.g. Iterative closest point (ICP)

## Slide 11: Bundler / Sparse Approach

## Slide 12: Minimal Geometric Problems
How do we calculate positions from images?
MGPs! http://cmp.felk.cvut.cz/mini/ (also recent VGS-IT by Tom Pajdla)
Given a bare minimum of data, get solution by applying some geometric constraints

## Slide 13: Minimal Geometric Problems
Five-point algorithm [Nister et al. 2004]
  Given five 2D points, find [R t] between the cameras
  Employs Epileptic geometry
    Fundamental matrix F = K2-T([t]×R)K1-1 = K2-TEK1-1
    Epipolar constraint x‘Fx = 0
    Solve 10th order polynomial meh
    Decompose E to R and t multiple (im)possible solutions
X

## Slide 14: Minimal Geometric Problems
Perspective three Point (P3P) [Kneip et al. 2013]
  Given three 3D points and their 2D observations, find [R t] of the observing camera
  From knowledge of K, convert 2D observations to 3D directions
  Leads to quartic equation
  Up to four solutions

## Slide 15: Minimal Geometric Problems
Kabsch‘s algorithm [Kabsch 1976]
  Many variants (Coustias, Horn, Umeyama, …)
  Given two sets of 3D points, calculate [R t] that aligns them
  Calculate centroids and
  Translation t = c2 – c1
  Rotation derived from covariance as using A = USVT so actually not a minimal problem (but certainly a geometric one)

## Slide 16: BA Using Minimal Geometric Problems
Use 5-point algorithm to get [R t] of the first two cameras
Keep using P3P for each consecutive camera
Keep aligning and concatenating

## Slide 17: BA Using Minimal Geometric Problems
Use 5-point algorithm to get [R t] of the first two cameras
Keep using P3P for each consecutive camera
Keep aligning and concatenating
But …

## Slide 18: BA Using Minimal Geometric Problems
Use 5-point algorithm to get [R t] of the first two cameras
Keep using P3P for each consecutive camera
Keep aligning and concatenating
Use RANSAC to select the points for the MGPs
Not enough! Need to do maximum likelihood estimation (MLE)

## Slide 19: Problem Statement (II)
Bundle Adjustment
  We have a set of „cameras“
    Each described by a pose [R t], projection K
    Possibly also lens distortion paramaters l and function
  We have a set of observed points
    Each described by its position X
  We have a set of observations
    Link between point X, camera C
    Position of point in the image x
    Residual to minimize

## Slide 20: Problem Statement (II) – BA Graph Example
Guildford Cathedral
92 poses
57957 landmarks

## Slide 21: Problem Statement (II)
Simultaneous Localization and Mapping–SLAM
  We have a set of „robot poses“
    Each described by a [R t] matrix
  We may have a set of landmarks
    Each described by its position l
  We have a set of observations
    Odometry observations (links between two poses)
      Estimated distance travelled D (also a pose itself)
      Residual to minimize
    Landmark observations (pose-landmark links)
      „Measurement“ of the landmark (e.g. Range-bearing vector)
      Residual to minimize

## Slide 22: Problem Statement (II) – SLAM Graph Example
Victoria Park (Sydney)
6969 poses
151 landmarks

## Slide 23: Problem Statement (II)
In general, inference on graphical models
  Set of variables V, each contains state vector vl
  Set of edges E, each a triplet {ik, jk, ok}
    Where i and j are vectors containing vertex indices
  Minimize where and ⊕ are vectorial difference and composition operators (e.g. (inverse) matrix multiplication), subject to their precedence and commutativity

## Slide 24: Problem Statement (II)
In general, inference on graphical models
  Set of variables V, each contains state vector vl
  Set of edges E, each a triplet {ik, jk, ok}
    Where i and j are vectors containing vertex indices
  Minimize
  Problem: if there are different kinds of observations, how to make different comparable?
  Solution: where is information matrix (inverse covariance) for observation k

## Slide 25: Least Squares
Given a set of constraints (observations), find a solution that minimizes L2 error
For a linear over-determined problem (where the unknown is )
The error is , squared error is*
This error minimizes where the first derivative cancels
Differentiating by gives
Hence
is the Moore-Penrose pseudo-inverse
*Note that is a scalar, thus allowing summation .

## Slide 26: Weighted Linear Least Squares
Sometimes we want to weight the observations
Treated easily, as , where is a diagonal matrix containing the weights
The weights should be reciprocal variances of the estimated variables (inverse covariances if estimating vectorial quantities)
Can „bake“ weights into by using since (diagonal matrix)

## Slide 27: Solving Least Squares
By solving the normal equation
  The condition number of is greater than of
  If was sparse but any of its rows is full, is dense
By using orthogonal decompositions
  Notably SVD of , and where is conjugate transpose (equals if real)
  Obtaining as easy as inverting diagonal entries while skipping zeros
  So solve
    Slow to compute (expensive Householder reduction to bidiagonal form, followed by iterative diagonalization)
    May be more precise, can threshold S to reduce noise
  Sometimes, there is an additional constraint , then only use the smallest singular value, zero the rest

## Slide 28: Least Squares Demo (Matlab)
O = [0 1; 1 3; 2 3; 3 7];
% observations of some 1D function
% O(:,1) are the arguments, a
% O(:,2) are the desired fit values, b
% we are trying to estimate b = p + qa + ra^2
% where x = [p q r] is our unknown
m = length(O);
A = [ones(m, 1), O(:, 1), O(:, 1).^2];
% stack the equations (1p + aq + a^2r)
x = (A' * A) \ A' * O(:,2)
% solve normal equation (backslash = solve)
xx = linspace(min(O(:, 1)) - .5, max(O(:, 1)) + .5);
yy = x(1) + x(2) * xx + x(3) * (xx.^2);
% evaluate the estimated model
plot(O(:, 1), O(:, 2), '*k') % plot a-s, b-s
hold on
plot(xx, yy, '-r') % plot the fitted curve
hold off

## Slide 29: Least Squares Demo (Matlab)
O = [0 1; 1 3; 2 3; 3 7];
% observations of some 1D function
% O(:,1) are the arguments, a
% O(:,2) are the desired fit values, b
% we are trying to estimate b = p + qa + ra^2
% where x = [p q r] is our unknown
m = length(O);
A = [ones(m, 1), O(:, 1), O(:, 1).^2];
% stack the equations (1p + aq + a^2r)
[U,S,V] = svd(A); % take SVD of A
Splus = zeros(size(S')); % S' may be rectangular
n = size(A, 2); % length of the diagonal
Splus(1:n, 1:n) = diag(1 ./ diag(S))' % recip. diag.
x = V * Splus * U' * O(:,2)
% solve using SVD
xx = linspace(min(O(:, 1)) - .5, max(O(:, 1)) + .5);
yy = x(1) + x(2) * xx + x(3) * (xx.^2);
% evaluate the estimated model
plot(O(:, 1), O(:, 2), '*k') % plot a-s, b-s
hold on
plot(xx, yy, '-r') % plot the fitted curve
hold off

## Slide 30: Weighted Least Squares Demo (Matlab)
O = [0 1; 1 3; 2 3; 3 7];
% observations of some 1D function
% O(:,1) are the arguments, a
% O(:,2) are the desired fit values, b
W = diag([10 1 10 10])
% weights for the observations
m = length(O);
A = [ones(m, 1), O(:, 1), O(:, 1).^2];
% stack the equations (1p + aq + a^2r)
x = (A' * W * A) \ A' * W * O(:, 2)
% solve normal equation (backslash = solve)
xx = linspace(min(O(:, 1)) - .5, max(O(:, 1)) + .5);
yy = x(1) + x(2) * xx + x(3) * (xx.^2);
% evaluate the estimated model
plot(O(:, 1), O(:, 2), '*k') % plot a-s, b-s
hold on
plot(xx, yy, '-r') % plot the fitted curve
hold off

## Slide 31: Nonlinear Least Squares
The estimation for bundle adjustment is highly nonlinear (rotations, projections, …)
Formally, instead of linear we now have with nonlinear function
To minimize , we again set
Instead of directly getting , at iteration , we improve
To solve this, we shall
  Linearize the problem using Taylor expansion
  Assume Gaussian noise to be able to do that

## Slide 32: Nonlinear Least Squares
We call our linearization point
Approximate
The Jacobian changes with the linearization
At step , we solve linearized problem , , and that is a linear model!
Solve familiar
Note that also using Hessian would converge faster (this is 1st order method)

## Slide 33: Nonlinear Least Squares
Gauss-Newton algorithm
  Take initial guess of , set
  Repeat until end of time
    Linearize the system
    Calculate residual note the vectorial op
    Solve
    If then
      stop
    note the vectorial op
Unlike linear LS, we need initial guess
Sometimes, LLS can be used to estimate it
For BA, there are MGPs to take care of that

## Slide 34: Nonlinear Least Squares Demo (Matlab)
O = [0 1; 1 3; 2 3; 3 7]; % we are trying to estimate b = p + pqa + pqra^2
% observations of some 1D function % where x = [p q r] is our unknown
% O is vector of pairs arg. a and desired fit b % h(x) = p + pqa + pqra^2, J = dh(x) / dx = [1+qa+qra^2, pa+pra^2, qa^2]
% we use this parameterization to make it nonlinear (would work with linear
x = [1 -1 -.1]'; % too but would be able to optimize in a single step, which would be boring)
% guess 0x (deliberately a bad guess, to take a few steps)
plot(O(:, 1), O(:, 2), '*k') % plot a-s, b-s
hold on
xx = linspace(min(O(:, 1)) - .5, max(O(:, 1)) + .5);
for i = 1:10
yy = x(1) + x(1) * x(2) * xx + x(1) * x(2) * x(3) * (xx.^2);
plot(xx, yy, '-b') % plot the initial guess
% evaluate the initial guess
J = [1 + x(2) * O(:, 1) + x(2) * x(3) * O(:, 1).^2, ...
x(1) * O(:, 1) + x(1) * x(3) * O(:, 1).^2, x(1) * x(2) * O(:, 1).^2];
% calculate the Jacobian
db = O(:,2) - x(1) - O(:,1) * x(1) * x(2) - O(:,1).^2 * x(1) * x(2) * x(3);
% calculate current error vector
dx = (J' * J) \ J' * db; norm_dx = norm(dx)
% solve
if(norm_dx < 1e-6) % see if we optimize
break
end
x = x + dx % increment
end
yy = x(1) + x(1) * x(2) * xx + x(1) * x(2) * x(3) * (xx.^2);
plot(xx, yy, '-r') % plot the final in red
hold off

## Slide 35: Intermezzo I
And now for something completely different …

## Slide 36: Getting Derivatives
Can readily use Matlab’s symbolic toolbox
Can use a cookbook (e.g. [J. Blanco, 2010, A tutorial on se(3) transformation parameterizations and on-manifold optimization, (TR)].)
Derivatives know nothing about vectorial, so
When dealing with rotations, commutability becomes an issue, must match
„If rotations and translations commuted, we could simply do all our rotations in the morning, before leaving home.“

## Slide 37: Getting Derivatives
Worked example – pose SLAM
  We have two poses, and
  We want to avoid optimizing 4×4 matrices
  Internally, they are optimized as [axis-angle ]
  That gives us and
  We have and
  For NLS, we need
  Also, error
  Then update for each variable
  Recall that this is on graph

## Slide 38: Chain rule
A simple rule that allows decomposition of derivatives so instead of calculating long , we calculate much shorter and and multiply them numerically when evaluating
We typically calculate derivatives of , , and and chain rule the rest

## Slide 39: SLAM Derivatives Continued
Lets try to get a Jacobian of
syms r00 r01 r02 r10 r11 r12 r20 r21 r22 t0 t1 t2 real
R = [r00 r01 r02; r10 r11 r12; r20 r21 r22]
t = [t0 t1 t2]'
% we have a rotation matrix and a translation vector
qw = sqrt(1 + r00 + r11 + r22) / 2;
qx = (r21 - r12) / (4 * qw);
qy = (r02 - r20) / (4 * qw);
qz = (r10 - r01) / (4 * qw);
% simplified matrix to quaternion (would need several branches for numerical stability)
qnorm = simplify(sqrt([qx qy qz] * [qx qy qz]'));
halfangle = asin(qnorm);
% get half of the rotation angle
ax = simplify(qx / qnorm * 2 * halfangle);
ay = simplify(qy / qnorm * 2 * halfangle);
az = simplify(qz / qnorm * 2 * halfangle);
% get the rotation as axis-angle
vec = [ax ay az t0 t1 t2]'
Rtvec = [r00 r01 r02 r10 r11 r12 r20 r21 r22 t0 t1 t2]';
J = simplify(jacobian(vec, Rtvec));
% let matlab calculate the derivatives
ccode(J)
% export to C

## Slide 40: The output of ccode() I
55 kB

## Slide 41: SLAM Derivatives Continued
Some more tricks
syms qnorm_ qx_ qy_ qz_ qw_ ax_ ay_ az_ real
J = subs(J, ax, ax_)
J = subs(J, ay, ay_)
J = subs(J, az, az_)
J = subs(J, qx, qx_)
J = subs(J, qy, qy_)
J = subs(J, qz, qz_)
J = subs(J, qw, qw_)
J = subs(J, qnorm, qnorm_)
% try substituting common subexpressions to tame the beast (don’t simplify J in the previous slide!)
ccode(J)
% export to C
Still generates 34 kB of C code
Gotcha – simple() and simplify() are different
Lesson learned – don’t use [R t], use Quaternions instead!

## Slide 42: The output of ccode() II
34 kB

## Slide 43: SLAM Derivatives Continued
Better yet
quat_t = [qw qx qy qz t0 t1 t2]
J0 = jacobian(quat_t, Rtvec);
%
syms ax_ ay_ az_ qx_ qy_ qz_ qw_ real
%qnorm = (sqrt([qx qy qz] * [qx qy qz]')); % MATLAB trolls you if U no careful …
qnorm = (sqrt(qx^2 + qy^2 + qz^2));
halfangle_ = asin(qnorm_);
ax_ = (qx_ / qnorm_ * 2 * halfangle_);
ay_ = (qy_ / qnorm_ * 2 * halfangle_);
az_ = (qz_ / qnorm_ * 2 * halfangle_);
vec_ = [ax_ ay_ az_ t0 t1 t2]'
quat_t_ = [qw_ qx_ qy_ qz_ t0 t1 t2]
J1 = jacobian(vec_, quat_t_);
% calculate the jacobians separately (note how J1 is on separate variables)
% chain rule as:
% f( g(R))' = f'( g(R)) * g'(R)
% aa(quat(R))' = aa'(quat(R)) * quat'(R)
% J = J1 * J0
J1 = subs(J1, qx_, qx); J1 = subs(J1, qy_, qy); J1 = subs(J1, qz_, qz); J1 = subs(J1, qw_, qw)
% substitute the quaternion to J1 (in practice, we would substitute *values* rather than *formulas*)
error = simplify(J - J1 * J0) % verify, this prints a matrix of zeros
Generates 1.94 and 2.29 kB of C for J0 and J1

## Slide 44: The output of ccode() III
T[0][0] = -(r21-r12)/sqrt(pow(1.0+r00+r11+r22,3.0))/4.0; T[0][1] = 0.0; T[0][2] = 0.0; T[0][3] = 0.0; T[0][4] = -(r21-r12)/sqrt(pow(1.0+r00+r11+r22,3.0))/4.0; T[0][5] = -1/(sqrt(1.0+r00+r11+r22))/2.0; T[0][6] = 0.0; T[0][7] = 1/(sqrt(1.0+r00+r11+r22))/2.0; T[0][8] = -(r21-r12)/sqrt(pow(1.0+r00+r11+r22,3.0))/4.0; T[0][9] = 0.0; T[0][10] = 0.0; T[0][11] = 0.0; T[1][0] = -(r02-r20)/sqrt(pow(1.0+r00+r11+r22,3.0))/4.0; T[1][1] = 0.0; T[1][2] = 1/(sqrt(1.0+r00+r11+r22))/2.0; T[1][3] = 0.0; T[1][4] = -(r02-r20)/sqrt(pow(1.0+r00+r11+r22,3.0))/4.0; T[1][5] = 0.0; T[1][6] = -1/(sqrt(1.0+r00+r11+r22))/2.0; T[1][7] = 0.0; T[1][8] = -(r02-r20)/sqrt(pow(1.0+r00+r11+r22,3.0))/4.0; T[1][9] = 0.0; T[1][10] = 0.0; T[1][11] = 0.0; T[2][0] = -(r10-r01)/sqrt(pow(1.0+r00+r11+r22,3.0))/4.0; T[2][1] = -1/(sqrt(1.0+r00+r11+r22))/2.0; T[2][2] = 0.0; T[2][3] = 1/(sqrt(1.0+r00+r11+r22))/2.0; T[2][4] = -(r10-r01)/sqrt(pow(1.0+r00+r11+r22,3.0))/4.0; T[2][5] = 0.0; T[2][6] = 0.0; T[2][7] = 0.0; T[2][8] = -(r10-r01)/sqrt(pow(1.0+r00+r11+r22,3.0))/4.0; T[2][9] = 0.0; T[2][10] = 0.0; T[2][11] = 0.0; T[3][0] = 0.0; T[3][1] = 0.0; T[3][2] = 0.0; T[3][3] = 0.0; T[3][4] = 0.0; T[3][5] = 0.0; T[3][6] = 0.0; T[3][7] = 0.0; T[3][8] = 0.0; T[3][9] = 1.0; T[3][10] = 0.0; T[3][11] = 0.0; T[4][0] = 0.0; T[4][1] = 0.0; T[4][2] = 0.0; T[4][3] = 0.0; T[4][4] = 0.0; T[4][5] = 0.0; T[4][6] = 0.0; T[4][7] = 0.0; T[4][8] = 0.0; T[4][9] = 0.0; T[4][10] = 1.0; T[4][11] = 0.0; T[5][0] = 0.0; T[5][1] = 0.0; T[5][2] = 0.0; T[5][3] = 0.0; T[5][4] = 0.0; T[5][5] = 0.0; T[5][6] = 0.0; T[5][7] = 0.0; T[5][8] = 0.0; T[5][9] = 0.0; T[5][10] = 0.0; T[5][11] = 1.0;
T[0][0] = 2.0/sqrt(qx_*qx_+qy_*qy_+qz_*qz_)*asin(sqrt(qx_*qx_+qy_*qy_+qz_*qz_))-2.0*qx_*qx_/sqrt(pow(qx_*qx_+qy_*qy_+qz_*qz_,3.0))*asin(sqrt(qx_*qx_+qy_*qy_+qz_*qz_))+2.0*qx_*qx_/(qx_*qx_+qy_*qy_+qz_*qz_)/sqrt(1.0-qx_*qx_-qy_*qy_-qz_~*qz_); T[0][1] = -2.0*qx_/sqrt(pow(qx_*qx_+qy_*qy_+qz_*qz_,3.0))*asin(sqrt(qx_*qx_~+qy_*qy_+qz_*qz_))*qy_+2.0*qx_/(qx_*qx_+qy_*qy_+qz_*qz_)*qy_/sqrt(1.0-qx_*qx_~-qy_*qy_-qz_*qz_); T[0][2] = -2.0*qx_/sqrt(pow(qx_*qx_+qy_*qy_+qz_*qz_,3.0))*asin(sqrt(qx_*qx_~+qy_*qy_+qz_*qz_))*qz_+2.0*qx_/(qx_*qx_+qy_*qy_+qz_*qz_)*qz_/sqrt(1.0-qx_*qx_~-qy_*qy_-qz_*qz_); T[0][3] = 0.0; T[0][4] = 0.0; T[0][5] = 0.0; T[1][0] = -2.0*qx_/sqrt(pow(qx_*qx_+qy_*qy_+qz_*qz_,3.0))*asin(sqrt(qx_*qx_~+qy_*qy_+qz_*qz_))*qy_+2.0*qx_/(qx_*qx_+qy_*qy_+qz_*qz_)*qy_/sqrt(1.0-qx_*qx_~-qy_*qy_-qz_*qz_); T[1][1] = 2.0/sqrt(qx_*qx_+qy_*qy_+qz_*qz_)*asin(sqrt(qx_*qx_+qy_*qy_+qz_*qz_))-2.0*qy_*qy_/sqrt(pow(qx_*qx_+qy_*qy_+qz_*qz_,3.0))*asin(sqrt(qx_*qx_+qy_*qy_+qz_*qz_))+2.0*qy_*qy_/(qx_*qx_+qy_*qy_+qz_*qz_)/sqrt(1.0-qx_*qx_-qy_*qy_-qz_~*qz_); T[1][2] = -2.0*qy_/sqrt(pow(qx_*qx_+qy_*qy_+qz_*qz_,3.0))*asin(sqrt(qx_*qx_~+qy_*qy_+qz_*qz_))*qz_+2.0*qy_/(qx_*qx_+qy_*qy_+qz_*qz_)*qz_/sqrt(1.0-qx_*qx_~-qy_*qy_-qz_*qz_); T[1][3] = 0.0; T[1][4] = 0.0; T[1][5] = 0.0; T[2][0] = -2.0*qx_/sqrt(pow(qx_*qx_+qy_*qy_+qz_*qz_,3.0))*asin(sqrt(qx_*qx_~+qy_*qy_+qz_*qz_))*qz_+2.0*qx_/(qx_*qx_+qy_*qy_+qz_*qz_)*qz_/sqrt(1.0-qx_*qx_~-qy_*qy_-qz_*qz_); T[2][1] = -2.0*qy_/sqrt(pow(qx_*qx_+qy_*qy_+qz_*qz_,3.0))*asin(sqrt(qx_*qx_~+qy_*qy_+qz_*qz_))*qz_+2.0*qy_/(qx_*qx_+qy_*qy_+qz_*qz_)*qz_/sqrt(1.0-qx_*qx_~-qy_*qy_-qz_*qz_); T[2][2] = 2.0/sqrt(qx_*qx_+qy_*qy_+qz_*qz_)*asin(sqrt(qx_*qx_+qy_*qy_+qz_*qz_))-2.0*qz_*qz_/sqrt(pow(qx_*qx_+qy_*qy_+qz_*qz_,3.0))*asin(sqrt(qx_*qx_+qy_*qy_+qz_*qz_))+2.0*qz_*qz_/(qx_*qx_+qy_*qy_+qz_*qz_)/sqrt(1.0-qx_*qx_-qy_*qy_-qz_~*qz_); T[2][3] = 0.0; T[2][4] = 0.0; T[2][5] = 0.0; T[3][0] = 0.0; T[3][1] = 0.0; T[3][2] = 0.0; T[3][3] = 1.0; T[3][4] = 0.0; T[3][5] = 0.0; T[4][0] = 0.0; T[4][1] = 0.0; T[4][2] = 0.0; T[4][3] = 0.0; T[4][4] = 1.0; T[4][5] = 0.0; T[5][0] = 0.0; T[5][1] = 0.0; T[5][2] = 0.0; T[5][3] = 0.0; T[5][4] = 0.0; T[5][5] = 1.0;
4 kB

## Slide 45: Matlab - Eliminating Common Subexpressions
syms temp0 temp1 temp2 temp3 real
subexpr(J0, 'temp0')
>> temp0 =
>> 1+r00+r11+r22
>> J0 =
>> [ -1/4*(r21-r12)/temp0^(3/2), 0, …
subexpr(ans, 'temp1')
subexpr(ans, 'temp2')
…
J0_ = ans;
ccode(temp0)
ccode(temp1)
ccode(temp2)
ccode(J0_)

## Slide 46: The output of ccode() IV
T.setZero(); temp5 = 1.0+r00+r11+r22; temp6 = sqrt(temp5); temp7 = pow(temp5, 3.0/2);
T[0][0] = -(r21-r12)/temp7/4.0; T[0][4] = -(r21-r12)/temp7/4.0; T[0][5] = -0.5/temp6;
T[0][7] = 0.5/temp6; T[0][8] = -(r21-r12)/temp7/4.0; T[1][0] = -(r02-r20)/temp7/4.0;
T[1][2] = 0.5/temp6; T[1][4] = -(r02-r20)/temp7/4.0; T[1][6] = -0.5/temp6;
T[1][8] = -(r02-r20)/temp7/4.0; T[2][0] = -(r10-r01)/temp7/4.0; T[2][1] = -0.5/temp6;
T[2][3] = 0.5/temp6; T[2][4] = -(r10-r01)/temp7/4.0; T[2][8] = -(r10-r01)/temp7/4.0;
T[3][9] = 1.0; T[4][10] = 1.0; T[5][11] = 1.0;
T.setZero(); temp0 = qx_*qx_+qy_*qy_+qz_*qz; temp1 = sqrt(temp0); temp2 = asin(temp1); temp3 = sqrt(1.0-temp0); temp4 = sqrt(pow(temp0,3.0))*temp2;
T[0][0] = 2.0/temp1*temp2-2.0*qx_*qx_/temp4+2.0*qx_*qx_/(temp0)/temp3;
T[0][1] = -2.0*qx_/temp4*qy_+2.0*qx_/(temp0)*qy_/temp3;
T[0][2] = -2.0*qx_/temp4*qz_+2.0*qx_/(temp0)*qz_/temp3;
T[1][0] = -2.0*qx_/temp4*qy_+2.0*qx_/(temp0)*qy_/temp3;
T[1][1] = 2.0/temp1*temp2-2.0*qy_*qy_/temp4+2.0*qy_*qy_/(temp0)/temp3;
T[1][2] = -2.0*qy_/temp4*qz_+2.0*qy_/(temp0)*qz_/temp3;
T[2][0] = -2.0*qx_/temp4*qz_+2.0*qx_/(temp0)*qz_/temp3;
T[2][1] = -2.0*qy_/temp4*qz_+2.0*qy_/(temp0)*qz_/temp3;
T[2][2] = 2.0/temp1*temp2-2.0*qz_*qz_/temp4+2.0*qz_*qz_/(temp0)/temp3;
T[3][3] = 1.0; T[4][4] = 1.0; T[5][5] = 1.0;
1 kB

## Slide 47: Numerical Differentiation
Much easier for fast prototyping
Typically not horribly imprecise but can be slow
Vector6d x1, x2; // the two variables
Vector6d expectation = x1 ⊖ x2; // the function we’re differentiating
Matrix6d J1; // derivative w.r.t. x1
for(int i = 0; i < 6; ++ i) {
Vector6d eps;
eps.setZero(); eps(i) = 1e-9;
Vector6d shift1 = eps ⊕ x1; // apply infinitesimal shift (ordering!)
Vector6d value = shift1 ⊖ x2; // see how that changes the output
J1.col(i) = (value - expectation) * 1e+9; // note cwise op
}
// do the same for x2

## Slide 48: Dual Numbers
Also good for prototyping but quite slow
A bit like complex numbers, with special semantics (while , we use )
Consider , inject
Evaluate using our “complex” arithmetics
For functions of multiple arguments, we need to put in each argument separately and re-evaluate several times
Rules for multiplication, division, transcendentals (can derive from Taylor series)
value
derivative

## Slide 49: Lie Group Basics
Groups on differentiable manifolds
Lie group SE(3) and associated algebra 𝔰𝔢(3)
SE(3) maps to Euclidean space 𝔼3 ([R t] are in it)
𝔰𝔢(3) is the tangent space of real skew-symmetric 4×4 matrices
Exponential map goes from 𝔰𝔢(3) to SE(3)
Logarithmic map goes from SE(3) to 𝔰𝔢(3)
Vectorial operator* [x]v packs skew-sym to vec
Cross operator [x]× goes back to skew-sym
Lie bracket [x, y] = xy – yx (where x, y ∈ 𝔰𝔢(3))
*several different notations exist

## Slide 50: Lie Group Basics
Let’s have skew symmetric 𝔰𝔬(3) matrix ,
Now, thinking about matrix exponent with
So exponential map of 𝔰𝔬(3) yields R, which is orthogonal (i.e. rotation matrix, in SO(3))
There’s also a logarithm of matrix

## Slide 51: SO(3) Exponential Map
Following ,
Seems familiar? :)

## Slide 52: Lie Group Basics
Going back to derivatives, we can calculate derivatives of exp, log, (inverse) compose, just like we did for , , and
Much of that has nice closed form
As for least squares, we choose (vectorial) 𝔰𝔢(3) or 𝔰𝔦𝔪(3) as the internal representation
See Tom Drummond’s TooN library for gritty details and code (https://www.edwardrosten.com/cvd/toon/html-user/)

## Slide 53: Back to bundling
And now …

## Slide 54: Handling Severe Nonlinearity
Gauss-Newton only computes step from local gradient, never looks back
Rosenbrock
Chebyshev
This would happen more with gradient descent. This is illustrative.

## Slide 55: Handling Severe Nonlinearity
Several algorithms that address this
Levenberg-Marquardt
Recall ordinary NLS
  We’re more or less doing ~
  We can control step size by magnitude of
Levenberg-Marquardt NLS with common choices or
Changing the value of inversely proportionally controls step size and direction choosing between GN and steepest descent

## Slide 56: Gauss & Newton Descending a Really Steep Gradient, Holding Hands
GN typically converges faster
GD less prone to get stuck but tends to zigzag a lot
GN
GD

## Slide 57: Gauss & Newton Descending a Really Steep Gradient, Holding Hands
GN typically converges faster
GD less prone to get stuck but tends to zigzag a lot
GN
GD

## Slide 58: Effects of Levenberg-Marquardt Damping
O = [0 1; 1 3; 2 3; 3 7]; % we are trying to estimate b = p + pqa + pqra^2
% observations of some 1D function % where x = [p q r] is our unknown
% O is vector of pairs arg. a and desired fit b % h(x) = p + pqa + pqra^2, J = dh(x) / dx = [1+qa+qra^2, pa+pra^2, qa^2]
% we use this parameterization to make it nonlinear (would work with linear
x = [1 -1 -.1]'; % too but would be able to optimize in a single step, which would be boring)
% guess 0x (deliberately a bad guess, to take a few steps)
plot(O(:, 1), O(:, 2), '*k') % plot a-s, b-s
hold on
xx = linspace(min(O(:, 1)) - .5, max(O(:, 1)) + .5);
for i = 1:100
yy = x(1) + x(1) * x(2) * xx + x(1) * x(2) * x(3) * (xx.^2);
plot(xx, yy, '-b') % plot the initial guess
% evaluate the initial guess
J = [1 + x(2) * O(:, 1) + x(2) * x(3) * O(:, 1).^2, ...
x(1) * O(:, 1) + x(1) * x(3) * O(:, 1).^2, x(1) * x(2) * O(:, 1).^2];
% calculate the Jacobian
db = O(:,2) - x(1) - O(:,1) * x(1) * x(2) - O(:,1).^2 * x(1) * x(2) * x(3);
% calculate current error vector
dx = (J' * J + 0 * eye(size(J, 2))) \ J' * db; norm_dx = norm(dx)
% solve
if(norm_dx < 1e-6) % see if we optimize
break
end
x = x + dx % increment
end
yy = x(1) + x(1) * x(2) * xx + x(1) * x(2) * x(3) * (xx.^2);
plot(xx, yy, '-r') % plot the final in red
hold off

## Slide 59: Effects of Levenberg-Marquardt Damping
O = [0 1; 1 3; 2 3; 3 7]; % we are trying to estimate b = p + pqa + pqra^2
% observations of some 1D function % where x = [p q r] is our unknown
% O is vector of pairs arg. a and desired fit b % h(x) = p + pqa + pqra^2, J = dh(x) / dx = [1+qa+qra^2, pa+pra^2, qa^2]
% we use this parameterization to make it nonlinear (would work with linear
x = [1 -1 -.1]'; % too but would be able to optimize in a single step, which would be boring)
% guess 0x (deliberately a bad guess, to take a few steps)
plot(O(:, 1), O(:, 2), '*k') % plot a-s, b-s
hold on
xx = linspace(min(O(:, 1)) - .5, max(O(:, 1)) + .5);
for i = 1:100
yy = x(1) + x(1) * x(2) * xx + x(1) * x(2) * x(3) * (xx.^2);
plot(xx, yy, '-b') % plot the initial guess
% evaluate the initial guess
J = [1 + x(2) * O(:, 1) + x(2) * x(3) * O(:, 1).^2, ...
x(1) * O(:, 1) + x(1) * x(3) * O(:, 1).^2, x(1) * x(2) * O(:, 1).^2];
% calculate the Jacobian
db = O(:,2) - x(1) - O(:,1) * x(1) * x(2) - O(:,1).^2 * x(1) * x(2) * x(3);
% calculate current error vector
dx = (J' * J + 1 * eye(size(J, 2))) \ J' * db; norm_dx = norm(dx)
% solve
if(norm_dx < 1e-6) % see if we optimize
break
end
x = x + dx % increment
end
yy = x(1) + x(1) * x(2) * xx + x(1) * x(2) * x(3) * (xx.^2);
plot(xx, yy, '-r') % plot the final in red
hold off

## Slide 60: Effects of Levenberg-Marquardt Damping
O = [0 1; 1 3; 2 3; 3 7]; % we are trying to estimate b = p + pqa + pqra^2
% observations of some 1D function % where x = [p q r] is our unknown
% O is vector of pairs arg. a and desired fit b % h(x) = p + pqa + pqra^2, J = dh(x) / dx = [1+qa+qra^2, pa+pra^2, qa^2]
% we use this parameterization to make it nonlinear (would work with linear
x = [1 -1 -.1]'; % too but would be able to optimize in a single step, which would be boring)
% guess 0x (deliberately a bad guess, to take a few steps)
plot(O(:, 1), O(:, 2), '*k') % plot a-s, b-s
hold on
xx = linspace(min(O(:, 1)) - .5, max(O(:, 1)) + .5);
for i = 1:100
yy = x(1) + x(1) * x(2) * xx + x(1) * x(2) * x(3) * (xx.^2);
plot(xx, yy, '-b') % plot the initial guess
% evaluate the initial guess
J = [1 + x(2) * O(:, 1) + x(2) * x(3) * O(:, 1).^2, ...
x(1) * O(:, 1) + x(1) * x(3) * O(:, 1).^2, x(1) * x(2) * O(:, 1).^2];
% calculate the Jacobian
db = O(:,2) - x(1) - O(:,1) * x(1) * x(2) - O(:,1).^2 * x(1) * x(2) * x(3);
% calculate current error vector
dx = (J' * J + 10 * eye(size(J, 2))) \ J' * db; norm_dx = norm(dx)
% solve
if(norm_dx < 1e-6) % see if we optimize
break
end
x = x + dx % increment
end
yy = x(1) + x(1) * x(2) * xx + x(1) * x(2) * x(3) * (xx.^2);
plot(xx, yy, '-r') % plot the final in red
hold off

## Slide 61: Effects of Levenberg-Marquardt Damping
O = [0 1; 1 3; 2 3; 3 7]; % we are trying to estimate b = p + pqa + pqra^2
% observations of some 1D function % where x = [p q r] is our unknown
% O is vector of pairs arg. a and desired fit b % h(x) = p + pqa + pqra^2, J = dh(x) / dx = [1+qa+qra^2, pa+pra^2, qa^2]
% we use this parameterization to make it nonlinear (would work with linear
x = [1 -1 -.1]'; % too but would be able to optimize in a single step, which would be boring)
% guess 0x (deliberately a bad guess, to take a few steps)
plot(O(:, 1), O(:, 2), '*k') % plot a-s, b-s
hold on
xx = linspace(min(O(:, 1)) - .5, max(O(:, 1)) + .5);
for i = 1:100
yy = x(1) + x(1) * x(2) * xx + x(1) * x(2) * x(3) * (xx.^2);
plot(xx, yy, '-b') % plot the initial guess
% evaluate the initial guess
J = [1 + x(2) * O(:, 1) + x(2) * x(3) * O(:, 1).^2, ...
x(1) * O(:, 1) + x(1) * x(3) * O(:, 1).^2, x(1) * x(2) * O(:, 1).^2];
% calculate the Jacobian
db = O(:,2) - x(1) - O(:,1) * x(1) * x(2) - O(:,1).^2 * x(1) * x(2) * x(3);
% calculate current error vector
dx = (J' * J + 100 * eye(size(J, 2))) \ J' * db; norm_dx = norm(dx)
% solve
if(norm_dx < 1e-6) % see if we optimize
break
end
x = x + dx % increment
end
yy = x(1) + x(1) * x(2) * xx + x(1) * x(2) * x(3) * (xx.^2);
plot(xx, yy, '-r') % plot the final in red
hold off

## Slide 62: Effects of Levenberg-Marquardt Damping
O = [0 1; 1 3; 2 3; 3 7]; % we are trying to estimate b = p + pqa + pqra^2
% observations of some 1D function % where x = [p q r] is our unknown
% O is vector of pairs arg. a and desired fit b % h(x) = p + pqa + pqra^2, J = dh(x) / dx = [1+qa+qra^2, pa+pra^2, qa^2]
% we use this parameterization to make it nonlinear (would work with linear
x = [1 -1 -.1]'; % too but would be able to optimize in a single step, which would be boring)
% guess 0x (deliberately a bad guess, to take a few steps)
plot(O(:, 1), O(:, 2), '*k') % plot a-s, b-s
hold on
xx = linspace(min(O(:, 1)) - .5, max(O(:, 1)) + .5);
for i = 1:100
yy = x(1) + x(1) * x(2) * xx + x(1) * x(2) * x(3) * (xx.^2);
plot(xx, yy, '-b') % plot the initial guess
% evaluate the initial guess
J = [1 + x(2) * O(:, 1) + x(2) * x(3) * O(:, 1).^2, ...
x(1) * O(:, 1) + x(1) * x(3) * O(:, 1).^2, x(1) * x(2) * O(:, 1).^2];
% calculate the Jacobian
db = O(:,2) - x(1) - O(:,1) * x(1) * x(2) - O(:,1).^2 * x(1) * x(2) * x(3);
% calculate current error vector
dx = (J' * J + 1000 * eye(size(J, 2))) \ J' * db; norm_dx = norm(dx)
% solve
if(norm_dx < 1e-6) % see if we optimize
break
end
x = x + dx % increment
end
yy = x(1) + x(1) * x(2) * xx + x(1) * x(2) * x(3) * (xx.^2);
plot(xx, yy, '-r') % plot the final in red
hold off

## Slide 63: Effects of Levenberg-Marquardt Damping
O = [0 1; 1 3; 2 3; 3 7]; % we are trying to estimate b = p + pqa + pqra^2
% observations of some 1D function % where x = [p q r] is our unknown
% O is vector of pairs arg. a and desired fit b % h(x) = p + pqa + pqra^2, J = dh(x) / dx = [1+qa+qra^2, pa+pra^2, qa^2]
% we use this parameterization to make it nonlinear (would work with linear
x = [1 -1 -.1]'; % too but would be able to optimize in a single step, which would be boring)
% guess 0x (deliberately a bad guess, to take a few steps)
plot(O(:, 1), O(:, 2), '*k') % plot a-s, b-s
hold on
xx = linspace(min(O(:, 1)) - .5, max(O(:, 1)) + .5);
for i = 1:1000
yy = x(1) + x(1) * x(2) * xx + x(1) * x(2) * x(3) * (xx.^2);
plot(xx, yy, '-b') % plot the initial guess
% evaluate the initial guess
J = [1 + x(2) * O(:, 1) + x(2) * x(3) * O(:, 1).^2, ...
x(1) * O(:, 1) + x(1) * x(3) * O(:, 1).^2, x(1) * x(2) * O(:, 1).^2];
% calculate the Jacobian
db = O(:,2) - x(1) - O(:,1) * x(1) * x(2) - O(:,1).^2 * x(1) * x(2) * x(3);
% calculate current error vector
dx = (J' * J + 1000 * eye(size(J, 2))) \ J' * db; norm_dx = norm(dx)
% solve
if(norm_dx < 1e-6) % see if we optimize
break
end
x = x + dx % increment
end
yy = x(1) + x(1) * x(2) * xx + x(1) * x(2) * x(3) * (xx.^2);
plot(xx, yy, '-r') % plot the final in red
hold off

## Slide 64: Levenberg-Marquardt
To control step size, use optimization gain with linear model error and squared error
If the gain is positive, take the step, reduce
If the gain is negative, keep the current linearization and increase at exponential rate with each failed step
See [Madsen, 1999, Methods for NLS Problems] for further details

## Slide 65: Pop Quiz Interlude
Quick, shout answer to win sausage!
Mike Powell was:
  Cat lady
  Hotdog eating champion
  Golfer
  Computer Scienceman

## Slide 66: Dogleg optimizer
Powell’s Dogleg (there’s also subspace Dogleg)

## Slide 67: Powell’s Dogleg Optimizer
Change gradient direction based on magnitude of , generate step of specified size
In solving the ordinary normal equation we can recover and also with
ΔxGN
ΔxSD
ΔxGN
ΔxGN
ΔxSD
ΔxSD
SD large
GN small
between trust radius

## Slide 68: Powell’s Dogleg Optimizer
Formally, for trust radius , the step is where with , and
is changed based on optimization gain
The initial trust radius can be large (unlike LM, DL does not resolve the lin. system on bad step)

## Slide 69: Handling Outliers – Robust Estimation
Outliers are a problem in computer vision
  Bad feature matching (mismatched feature)
  Reflections (matched to a good feature in a mirror)
  Moving objects (cars, pedestrians, wind)
Can try to reject suspicious observations
Can use robust estimation

## Slide 70: Robust Estimation
Try to identify outliers in the LS framework
LS minimize squared error big outliers have huge (squared) influence
Try to generalize the error where is ordinary LS loss function

## Slide 71: Robust Estimation
Try to minimize pseudo-L1 error
Huber kernel

## Slide 72: Normal Equations for Robust Estimation
So how to plug it in? Notice that for LS, and
The derivative of loss is score function
This can be used for weights, where
Let’s try setting

## Slide 73: Robust Least Squares Demo (Matlab)
O = [0 1; 1 3; 2 3; 2.5 4.9; 3 7];
% observations of some 1D function
% O(:,1) are the arguments, a
% O(:,2) are the desired fit values, b
a = 1.345;
% guess some parameter for outlier rejection
for i = 1:10
J = … % calculate the Jacobian
db = … % calculate current error vector
w = zeros(length(db), 1);
for j = 1:length(db)
u = db(j);
if(abs(u) <= a)
w(j) = 1 / u; % resolve division by zero
else
w(j) = a * sign(u) / u;
end
end
W = diag(w); % calculate the robust weights
dx = (J' * W * J) \ J' * W * db;
% solve normal equation (backslash = solve)
end
% [plot stuff]

## Slide 74: Solving Overfitting / Scale Problems
Now we‘re overfitting, the points at the bottom are all treated as outliers
Changing the value of is a temporary solution
We need to approximate scale of the problem
MAD (median absolute deviation)
Now set
Alternative to MAD - Huber‘s second proposal

## Slide 75: Robust Least Squares Demo (Matlab)
O = [0 1; 1 3; 2 3; 2.5 4.9; 3 7];
% observations of some 1D function
% O(:,1) are the arguments, a
% O(:,2) are the desired fit values, b
a = 1.345;
% guess some parameter for outlier rejection
for i = 1:10
% [calculate J, db]
MAD = median(abs(db));
s = 1.4826 * MAD;
% calculate MAD
w = zeros(length(db), 1);
for j = 1:length(db)
u = db(j) / s; % apply scale
if(abs(u) <= a)
w(j) = 1 / u; % resolve division by zero
else
w(j) = a * sign(u) / u;
end
end
W = diag(w); % calculate the robust weights
% [solve]
end
% [plot stuff]

## Slide 76: Robust Least Squares Demo (Matlab)
O = [0 1; 1 7; 2 3; 2.5 4.9; 3 7]; % turrn the second point into an OUTLIER
% observations of some 1D function
% O(:,1) are the arguments, a
% O(:,2) are the desired fit values, b
a = 1.345;
% guess some parameter for outlier rejection
for i = 1:10
% [calculate J, db]
MAD = median(abs(db));
s = 1.4826 * MAD;
% calculate MAD
w = zeros(length(db), 1);
for j = 1:length(db)
u = db(j) / s; % apply scale
if(abs(u) <= a)
w(j) = 1 / u; % resolve division by zero
else
w(j) = a * sign(u) / u;
end
end
W = diag(w); % calculate the robust weights
% [solve]
end
% [plot stuff]

## Slide 77: More About Robust Kernels
What are the magic numbers (1.4826, 1.345)?
Relative estimator efficiency where is true solution, is expectation
Typically compare to NLS, set efficiency to 95%

## Slide 78: More About Robust Kernels
Are there other kernel types?

## Slide 79: Intermezzo II
And now for something completely different …

## Slide 80: Solving Linear Systems
NLS boils down to solving linearized system
  Most of time is spent there
  In the remainder, let‘s assume
  In here, is sparse (most of its entries are zero) but many of the methods apply to dense matrices too

## Slide 81: Solving Linear Systems
Different methods
  Direct methods - reduce the matrix to triangular
    Proven complexity, mature algorithms
    Need considerable amounts of memory
  Iterative methods - do a lot of vector math, iteratively converge to the solution
    Needs very little memory
    Convergence depends on problem, preconditioner
    Quite young field, not much proven
  Subspace methods - use Eigenvalue-like algorithms to calculate subspace approximations, solve there
[Davis, 2006, Direct Methods for Sparse Systems]
[Saad, 2003, Iterative Methods for Sparse Systems]

## Slide 82: Direct Methods Primer
Consider the two following systems
In both cases,
What happened?
Pivoting for stability, cost. Only one r.h.s.

## Slide 83: Gaussian Elimination, Backsubstitution
A = round(rand(3,3) * 10)
b = round(rand(3,1) * 10)
n = length(A);
for k=1:n-1
for i=k+1:n
x = A(i,k) / A(k,k);
A(i,k+1:n) = A(i,k+1:n) - x * A(k,k+1:n); % row combine
A(i,k) = 0; % we just eliminated it
b(i) = b(i) - x * b(k);
end
end
A
b
% Gaussian elimination
x = zeros(n,1);
for i=n:-1:1 % loop backwards
r = b(i) - dot(A(i,i+1:n), x(i+1:n)');
x(i) = r / A(i, i);
end
x
% back-substitution

## Slide 84: LU decomposition
Another old method
Factorize
  being lower triangular with unit diagonal
  being upper triangular
To solve (and so )
  First solve L forward substitution w/o div
  Then solve back-substitution
To work, must be square, invertible
Will require pivoting for stability
  Partial (reorder rows)
  Full (reorder rows, cols)

## Slide 85: LU decomposition
A = round(rand(3,3) * 10)
LU = A; % works in-place
for k = 1:n
LU(k+1:n, k) = LU(k+1:n, k) / LU(k, k);
% divide by pivot (modifies the rest of this column)
for i = k+1:n
x = LU(i, k);
for j = k+1:n % explicit loop intended
LU(i, j) = LU(i, j) - x * LU(k, j); % causes fill-in in sparse version
end
% reduce the rest of the matrix
end
% modify the lower-right submatrix
end
U = triu(LU)
L = tril(LU, -1) + eye(size(LU))
% unpack to L and U, add identity diagonal to L

## Slide 86: LU decomposition
Several variants, based on ordering of loops i j k
read
write
kij
kji

## Slide 87: LU decomposition
In sparse version, we care about fill-in
Depends on order of rows / columns
A
L+U

## Slide 88: AMD Ordering
Approximate Minimum Degree [Amestoy 2004]

## Slide 89: Enter Captcha If Youre awake

## Slide 90: Cholesky factorization
Factorize
  being upper triangular, with positive diagonal entries
To solve
  First solve forward substitution
  Then solve back-substitution
To work, must be square, symmetric and positive-definite (SPD)
  NLS matrices are (up to numerical precision)
  Adding small damping on the diagonal usually helps
  Modified Cholesky factorization
Does not need pivoting

## Slide 91: Cholesky factorization
A = round(rand(3,3) * 10);
A = A' * A + eye(size(A)) * 10 % try to make it SPD
R = zeros(size(A));
for j = 1:n % for every column
for k = 1:j-1 % for all prev cols that are nnz at row j (know those from etree)
s = 0;
for i = 1:k-1 % for all blocks above the diagonal in the prev column
s = s + R(i, k) * R(i, j); % takes elements from two different columns
end
% cmod; causes fill-in in the current column
R(k, j) = (A(k, j) - s) / R(k, k); % accesses upper diagonal of A
end
s = R(1:j-1, j)' * R(1:j-1, j);
R(j, j) = sqrt(A(j, j) - s); % must be positive (or modified Cholesky)
% cdiv
end

## Slide 92: Sparse Cholesky
Elimination tree theory
  Calculate tree that drives loops in the factorization
  Saves time
  Particular orderings also yield elimination trees with independent and balanced subtrees (parallelism)
Supernodal Cholesky
  Sometimes, several columns in the factorization have identical nonzero structure - supernodes
  Treating supernodes as dense allows parallelism, GPU acceleration
Multifrontal Cholesky
  Frontal matrices, conceptually similar to supernodes

## Slide 93: Cholesky factorization - AMD again

## Slide 94: QR decomposition
Relatively new method (in the 60‘s)
Factorize
  can now be rectangular
  being orthogonal ()
  being upper triangular (zero rows at the bottom)
To solve
  First solve multiplication*
  Then solve back-substitution
No pivoting needed
Fill-in depends on column ordering only
  Out-of-core methods

## Slide 95: Computing QR decomposition
Similar to Gaussian elimination
Householder reflections
  Compute a reflection about a plane (mirror matrix) that zeroes a lower part of a column in R
  Minor tricks (sign choice) for numerical stability
  Record reflections rather than representing Q
Givens rotations
  Compute rotation matrix that zeros one element in R
  Record rotation chains rather than representing Q

## Slide 96: QR decomposition
Householder reflections

## Slide 97: Slide stolen from Michael Heath‘s lecture

## Slide 98: Slide stolen from Michael Heath‘s lecture

## Slide 99: QR decomposition
Related to Cholesky
  is the same as in Cholesky factorization, up to the sign of the rows (Cholesky always has positive diag)
Can directly solve NLS on without forming
  Numerical benefits

## Slide 100: Householder QR Demo (Matlab)
M = round(rand(5, 3) * 10)
[m n] = size(M);
Q = eye(m, m); % crime against QR: explicit Q
R = M; % works inplace
elim = min(m - 1, n); % decide how many cols to eliminate to get triangular R
for i = 1:elim
Aii = R(i, i);
Ai_norm = sqrt(R(i:m, i)' * R(i:m, i));
dii = abs(Ai_norm) * sign(sign(Aii) + 0.5); % !!! need zero-avoiding sign function !!!
wii = Aii - dii;
two_fi_inv_squared = -1 / (wii * dii);
% calculate Householder reflection of the i-th column
for j = i+1:n
fj = wii * R(i, j); % the head of column i is replaced by wii
fj = fj + R(i+1:m, i)' * R(i+1:m, j); % dot of lower-part of columns i and j
fj = fj * two_fi_inv_squared;
% calculate columns dot
R(i, j) = R(i, j) - fj * wii;
R(i+1:m, j) = R(i+1:m, j) - fj * R(i+1:m, i);
% update jth column
end
% apply Householder reflections also to the other columns to the right

## Slide 101: Householder QR Demo (Matlab)
for j = 1:m
fj = wii * Q(j, i); % the head of column i is replaced by wii
fj = fj + Q(j, i+1:m) * R(i+1:m, i); % dot of lower-part of columns i and j
fj = fj * two_fi_inv_squared;
% calculate columns dot
Q(j, i) = Q(j, i) - fj * wii;
Q(j, i+1:m) = Q(j, i+1:m) - fj * R(i+1:m, i)';
% update jth column
end
% apply Householder reflections also to the r.h.s columns, in transpose!
R(i, i) = dii;
R(i+1:m, i) = 0; % finally, clear the rest of the current column
end
% eliminate lower triangle of M, column by column

## Slide 102: Schur Complement Trick
In BA, it is possible to reorder the system to have diagonal submatrices
  bipartite ordering, MIS
57957×3
92×6
Λ
PΛP-1
*The sparsity is the same on the left / right. The nnz‘s are just very inflated to be visible and that makes the sparsity appear different.

## Slide 103: Schur Complement Trick
Then the matrix is partitioned as and the linear system partitioned as
with ,
The Schur complement of A is
92×6
92×6
<1% nnz
>40% nnz

## Slide 104: Schur Complement Trick
The linear system can be solved as
57957×3
92×6

## Slide 105: Schur Complement Trick

## Slide 106: iterative methods?
Who will do seminar on

## Slide 107: subspace methods?
Who will do seminar on

## Slide 108: Back to bundling
And now …

## Slide 109: Calculating Covariances
System covariances (variable covariances)
  Different from edge (observation) covariances
Obtained by inverting the information matrix Λ
  Inverse is fully dense
Λ

## Slide 110: Calculating Covariances
Use Cholesky factorization & backsubstitution, keep only parts of the covariance to save memory
  The way Google‘s Ceres does it, gruesome performance
Use SVD
  Another dead end explored by Google™

## Slide 111: Calculating Covariances
Use recursive formula for calculating only some parts of the inverse
[Björck, 1996, Numerical methods for least squares problems, SIAM]

## Slide 112: Calculating Covariances
Use recursive formula for calculating only some parts of the inverse
[Ila, 2015, Fast Covariance Recovery in Incremental Nonlinear Least Square Solvers, ICRA]

## Slide 113: Incremental Covariances
In SLAM, we often only have small increment
Updating covariance cheaper than recalculating from scratch where with
Need only a few elements of (can use backsubstitution)
[Ila, 2015, Fast Covariance Recovery in Incremental Nonlinear Least Square Solvers, ICRA]

## Slide 114: Visualizing Covariances

## Slide 115: Are you still alive?
The end